Campo Fire and Rescue – Station 86

Motorola XTL 5000 Mobile Radio

# Operations Manual

The Motorola 5000 Series Mobile Radio and 5000 Series Hand Held’s are the new primary dispatch radios for Campo Fire. They are a part of the San Diego County, 800Mhz Trunking system.

Radio ON / OFF

To turn the radio ON, press the PWR button on the front top left corner. The radio will remain dark for a few moments, and will then perform a SELF CHECK.

If you see a failure code, such as FL/## or ER/##, the radio may be defective. Turn the radio OFF, then back ON again. If you receive a failure code again, turn the radio OFF and turn it in for service.

To turn the radio OFF, press the PWR button again.

Set Volume

1.    Press and hold the Volume Rocker Switch to increase or decrease the volume. You will hear a Volume Set tone as you increase or decrease the volume.

Select A Talkgroup / Mode

- To select a Talkgroup / Mode, press the up ▲ or down ▼ Mode Select Rocker Switch until the desired talkgroup name is displayed.

Select a Zone

Zone Up

- Press the ZN UP or ZN DN until the desired zone name is displayed.

To transmit:

- Select the desired zone and talkgroup/mode. The selected
zone and talkgroup appear on the display.

- Listen for ongoing conversation. When talkgroup becomes
available, proceed with your call.

- Press the Push-To-Talk (PTT) on the microphone and wait for the Talk Permit Tones (3 quick beeps). Begin speaking with the microphone approximately 1" from your mouth.

a. If you hear a phone-type busy signal, release the PTT and wait for the system to call you back with the Call Back Tones (similar to the Talk Permit).

b.    If you hear a steady low-pitched tone (Honk), release the PTT and wait until the talkgroup is available. When the talkgroup is available you will hear the Talk Permit Tones. You now have priority in the queue and have  4 seconds to respond

4.   Release the PTT button to receive.

Scan ON/OFF

Note: If you turn the scan on and hear a continuous low tone with the words "EMPTY LIST" on the display, turn the scan off and program a scan list. Each "ZONE" requires its own scan list.

1.	To turn Scan ON, press the SCAN button momentarily. The
SCAN indicator lamp under the SCAN button will light up.

Scan

2.	To turn Scan OFF,	|	|

press the SCAN

button momentarily. The SCAN indicator lamp under the SCAN button will turn OFF.

Scan List Program

- Press and hold the SCAN button until you hear a single beep
tone. The SCAN indicator lamp will begin flashing.

- Use the ZN UP / ZN DN and Mode Rocker Switch to display the talkgroup you wish to scan.

- Press the SEL button once to add the displayed talkgroup to the scan list as a Non-Priority talkgroup.

3a. When the talkgroup is added as a Non-Priority, you will see N-PRI will light up on the display.

3b. To remove the talkgroup, press SEL again or the DEL button.

NOTE: Your radio has been pre-programmed to have whichever talkgroup you are selected to transmit on as your Priority 1 talkgroup. As you switch talkgroups to transmit, the new talkgroup becomes Priority 1.

4.	To add more talkgroups to the scan list, repeat Step 3. Your
radio can scan up to 10 talkgroups at any one time.

4a. If you attempt to program too many talkgroup into your scan list, the radio will emit a low-pitched tone. You must remove a talkgroup to add others to the scan list.

- Press HOME to exit.

View Scan List

1. Press and hold the SCAN button until you hear a single beep tone and the SCAN indicator begins to flash.

2. Press the RCL button to review each of the zones / talkgroups programmed into your scan list.

- Press the HOME key to exit.

Nuisance Delete

When a particular talkgroup you are scanning becomes annoying, you can temporarily delete the talkgroup from the scan list. This is called "Nuisance Delete."

- While scanning, wait until the talkgroup you wish to "Nuisance Delete" is receiving and is displayed. Press the DEL button.

- To un-delete deleted zones / talkgroups, turn scan OFF, then back on again, or turn the power off and back on again. All previously programmed talkgroups will now be scanned.

Display Lights ON/OFF

- Your radio display has 4 levels of display brightness intensity: High, Medium, Low, and OFF. Press the DIM button to lower the display intensity

NOTE; While the display and keyboard backlights are OFF, the radio is still fully operational.

- Press the DIM button again to return to High intensity.

Site Switch

NOTE: Your radio is programmed to automatically allow you to roam throughout the county, much like a cell phone system. There may be times, such as when the system goes into SITE TRUNKING, when you may wish to have your radio affiliate with a different mountaintop repeater site. (See the Field Reference Guide section System Conditions for more information.)

1.	Press the SIT (1) button briefly to display the current site with which your radio is affiliated.

la. The radio will display the repeater site you are affiliated with for approximately 2 seconds,

lb. The radio will then display the Received Signal Strength Indicator, or RSSI, and a number between 0 and 99. (Any number above 50 is considered good.)

1c. After approximately 2 seconds, the radio will return to normal operation.

- To force the radio to affiliate with a different repeater site, press and hold the SIT button until SCANNING appears in the display. The radio will attempt to affiliate with a different repeater site. The radio may affiliate with a different site, or it may re-affiliate with the same site.

- Repeat Step 1 to confirm which site you are now affiliated with. If you need to affiliate with a different site, repeat Steps 1 and 2 until you affiliate with an adequate site. Turning the radio on and then off will default it to the nearest site.

Direct Operation 

Your radio has the ability to operate directly with other radios on a conventional channel like “CNV”, without going through the repeaters.

Direct

NOTE: Remember that while operating in DIRECT, you will not be able to speak with your dispatcher or units a long distance away. DIRECT is only good for approximately 1-5 miles, depending on terrain, etc.

- Switch your radio to a conventional talkgroup.

- Press the DIR button. The DIR indicator lamp will light up.

To exit DIRECT operation, press the DIR button again.

Monitor

When you are on a

conventional talkgroup,

you should press the

monitor button (prior to

transmitting) to ensure

no one else is using the

same frequency. This is

especially important when using your radio away from the San Diego RCS area.

1.	Press the Mon (button “8” on the keypad) button to determine if the talkgroup is busy, or

a.  Press and hold the Monitor button for about 2 seconds to  ; lock the squelch open.

2.	When the talkgroup is clear, press the PTT button and speak into the microphone.