Bold type: Trunked systems    			Italic type: Conventional systems

Front Panel Controls

NOTE: The following controls are shown in Figure 1. Microphone - The microphone is located in this area. For best results, hold the transceiver 2-3 inches from your mouth and speak at a normal conversational level.

Display - This is a graphical LCD (Liquid Crystal Display). The display backlight is  turned  on when any key is pressed or when the Backlight option key is pressed

Up/Down Switch - Selects zones. Pressing the upper part of the switch selects the next higher number and pressing the lower part selects the next lower number. This control also provides up/down select in the menu mode and in other modes when up/down select is required.

F1 - In menu mode, functions as a step back and exit key.

F2 - Selects the menu mode .Also functions as an Enter or Select key in the menu and other modes.

F3 - Selects the Home talk group

F4 – Zone Select

DTMF Keypad – Used for zone selection with F4 key.

Speaker - The transceiver speaker is located near the bottom of the front panel. When a speaker/microphone is used, this speaker is automatically disabled.

Zone And Channel Select

The front panel Up/Down key changes and displays the current zone. When not in special modes such as the menu mode, pressing either the top or bottom part of this key once displays the current zone number as “Zone x”. Then quickly pressing it again changes the selected zone up or down. After the highest programmed zone is displayed, wrap-around to the lowest programmed zone occurs and vice versa. The selected zone is also displayed briefly on power up.

A zone may also be selected by pressing F4 followed by the zone number followed by F4.

Low Battery Indication

A low-battery condition is indicated by the icon in the display. The battery should be recharged or replaced as soon as practical after this indication appears. Once this indication appears, it stays on until power is cycled. The following additional low battery indications and conditions may be enabled by programming:

• A chirp sounds once a minute in the standby and transmit modes.

• A chirp sounds each time the PTT switch is pressed. • Top panel LED indicator flashes red every 30 seconds in the receive mode.

• Low power is selected when transmitting.

Mode (channel) Select

Channels are selected by the rotary 16-position switch on the top panel. The alias (identification) for the selected channel/group is displayed continuously during normal operation.

When an unprogrammed channel is selected, “UNPROGRAMD” is displayed and a tone sounds (if tones are enabled).

Selecting a Scan List

Conventional Operation - The scan list is user selectable.

SMARTNET/SmartZone (RCS) Operation - Each channel (talk group) is programmed to select one of programmed lists.

Select the scan list as follows:

Select first channel to be scanned.

With scanning disabled (Scan Off)  press F2, scroll to “Scan Edit”, press F2. List 1 appears.

F2 again – Channel appears in window.

F2 again (s) appears in upper left

Arrow up or down to next channel (do not use mode (channel) rotary selector)

F2 to add to scan list

Arrow up or down to next channel (do not use mode (channel) rotary selector)

F2 to add to scan list or F1 to finish

Enable scan list  s(can on)

2. The currently selected list is displayed as “List x”,

where “x” is the currently selected list. To exit without changing the selected list, simply press the Scan List option key again or the F1 or F2 key.Programming a Scan List

If the Scan Edit option key or menu parameter is programmed, conventional and SMARTNET/ SmartZone standard scan lists can be programmed as follows. Changes are permanent (cycling power does not reselect a default condition).

1. Make sure scanning is off ( icon not displayed). Select a conventional or SMARTNET/SmartZone channel corresponding to the scan list being programmed.

2. Select the scan edit mode using the Scan Edit option key or menu parameter. This mode is indicated by in the display.

3. If applicable, select the list to be edited by pressing the Up/Down switch. Select the desired list by pressing the F2 key. The selected list is indicated as “LIST x”. If user programming is disabled on a list, “NO EDIT” is momentarily displayed and it cannot be edited.

4. Select the channel you want to add or delete by pressing the Up/Down switch. After the last channel in the current zone is displayed, the first valid channel in the next zone is displayed and vice versa. Lists are limited to 16 channels. If an attempt is made to add more than 16, “LIST FULL” is displayed and a channel must be deleted before another can be added.

5. If the selected channel is in the scan list (scanned), the icon is displayed. To change the status of the displayed channel, press the F2 (Enter) key. With conventional channels only, if the selected scan list is programmed with a fixed priority channel (see page 18), the next press of F2 makes the current channel the priority channel. The icon is then displayed to indicate that it is the priority channel.

6. To exit this mode and save the changes, press the F1 (Exit) key.

There are four “fleets” in this radio: County-wide, San Diego City, conventional, and TRF. The radio cannot scan between fleets. Each fleet has its own scan list and cannot scan between fleets.

Nuisance Channel Add/Delete

With standard scanning, both conventional and SMARTNET/SmartZone channels can be temporarily deleted from the scan list. Proceed as follows to temporarily delete a nuisance channel:

1. While receiving a message on the channel to be deleted, press and hold the Scan option key until a tone sounds (about 2 seconds).

2. The channel is then deleted and scanning of the remaining channels in the scan list resumes.

3. Deleted channels are added back into the scan list if any of the following occur:

• Scanning is turned off and then on again using the Scan option key or menu parameter.

• Transceiver power is turned off and then on again.

• The selected channel is changed.