Campo Fire and Rescue – Station 86

Motorola XTS 5000 Portable

# Operations Manual ( Revised 12/27/2011)

The Motorola 5000 Series Mobile Radio and the Motorola 5000 Series Hand Held’s are the new primary radios for Campo Fire. They are a part of the San Diego County, 800Mhz Trunking system.

XTS 5000 Functional Controls

FIGURE 1

|  | FIGURE 2 Display indication when the XTS 5000 is turned on and our normal dispatch channel Zone HF3, Talkgroup Dispatch 2 (DISP 2) is selected. Note – All available Status Symbols are shown for illustration. Not all Status Symbols will be displayed at one time during normal operation. FIGURE 3 “dot softkeys” the 1, 2 or 3 dot Menu Select Buttons select the function shown over them on the display. As you change programming modes the function of these softkeys change to the function displayed above them. |
| --- | --- |

Normal Operation ( See FIGURE’s 1, 2 & 3 )

When powered up with the ON/OFF Volume Knob the 5000 should be on the “Home” (CF MV D 10A) channel. If the Home Zone is not displayed:

- Press the Single Dot key on the keypad under ZONE on the display. The first letter on the  display will flash on and off.

- Press the left or right arrow on the 4-way Navigation Button to select the CF Bank.

- Press the Home Button to select the CF Zone and rotate the 16-Position Select Knob until CF MV D 10A is displayed.

- Press the Push-To-Talk (PTT) button and wait for the Talk Permit Tones (3 quick beeps) before speaking

Campo Fire is normally assigned channels in this CF Bank. When a call is dispatched or paged Dispach will assign a Command and Tac frequency for the incident. Referencing the 800Mhz Frequency Map you will notice each command Channel is grouped with one or more Tac channels. A typical assignment would be “CF CMD 10C”. If you miss the assignment from Dispatch call them on  CF MV D 10A or the assigned Command Channel and ask what your Command and Tac assignments are. Remember – on the Fleet Map Channels are referred to as “MODES”.

To select a Command or Tac channel in the Home CF Bank rotate the 16-Position Select Knob until the desired channel is displayed. If you are assigned frequencies away from your Home Channels, follow the procedures 1 through 3 above to select the proper Zone and Channel.

Command Channel. When dispatched to an incident acknowledge your response and arrival at the scene, to the Dispatcher, on the Assigned Command Channel. Command is also used for status updates to Dispatch, by the Incident Commander and to request additional units or resources.

Tac Channel. Communications between units responding and crewmembers should be primarily on the Assigned Tac Channel.

Scanning, Use and Review. Place the Three Position toggle switch in the A position. To review the Zones and Channels (Modes) programmed to scan press the “3 dot” soft key under VIEW on the display and then press the “1 dot” soft key under SCAN.  The little square in the upper right of the display now indicates you are in the SCAN review or programming mode. Press the Left or Right  keys on the 4-way Navigation Button to review the Zones  and Channels setup to scan. Press the Home Button to return to normal operation. Note – You can scan multiple Zones and Channels outside of the normal HF3 Zone or the Zone you are assigned. During an active incident this may cause you to miss a call so, use the Scan function carefully.

Scanning, Programming. To program a Zone and/or Channels (Modes) within a Zone for scanning press the “2 dot” soft key under PROG and then the “1 dot” soft key under SCAN.  The little flashing square in the upper right of the display now indicates you are in the scan review or programming mode. ( The “3 dot” RCL button will review the Channels and Zones currently set to scan. )

To select a channel for scanning toggle the left or right 4-way Navigation Button until the desired channel is displayed. Press the “1 dot” SEL softkey. The “Z” will appear in the display indicating this channel is set to scan.  To delete a channel from the scan list press the “2 dot” DEL key. You can select up to 15 channels, per System, for scanning. If you exceed 15 selections you will receive an error beep. Press the Home Button to save your selections and return to normal operation.

NOTE. If you turn on the Scan function and you receive a low tone, and the display indicates “EMPTY LIST” you have no channels programmed for scan. Turn off the Scan switch and program a scan list.

Emergency Button. The Top Orange Button will send an emergency page message to  Dispatch with your unit number. You will be called immediately by the Dispatcher and asked the nature of your emergency. If you have hit this button accidentally (fool) you must cancel it by holding it for 2 seconds or till the beeping goes away. You will still need to transmit to the Dispatcher the nature of the emergency or the error of your ways.

IMPORTANT: Unlike the Law Enforcement radio system our 800Mhz radios are NOT equipped with GPS. This means if you hit the Emergency button aside from lots of bells no one knows where you are or what your emergency is. So, if you can move and talk notify an emergency with a voice call and leave the button for last resort.

Signal Strength and Coverage. There is a signal strength indicator on the display. If you are out of range the indicator bars will drop to none and the radio will emit a long, repeating, beep. Move your location or try your vehicle radio. In an emergency you can contact the California Division of Forestry (CDF) dispatcher (Monta Vista) on the Kenwood VHF radios. CDF can then relay your request to Heartland.

Setting the Clock / Date Time. Don’t bother. It doesn’t work. The clock indicates how long your radio has been turned on!

Mute Button press Tones. On the menu above there is a MUTE selection. When pressed this brings up the option to turn on or off the beep tone when any button is pressed.

Side Button #2.  Scan nuisance delete. Press to temporally disable a nuisance Channel (lots of chatter you don’t need to hear) during scanning. To cancel nuisance delete and resume normal scanning toggle the ABC switch to B or C and then back to the A position.

Direct operation. The CNV ( conventional ) channels can operate in Talkaround mode. That is local unit to unit without going through the repeaters. This mode can be used for local operations like traffic control or training, without tying up a repeater frequency. See figure 2. To set in non repeater mode program to the CNV ZONE and then set it with the HOME key. Turn the Channel Select Knob to the desired channel. Push the PROG soft key, select the DIR menu. On the DIR menu select DIR to enter Talkaround mode. The Talkaround symbol will appear on the display. Some channels default to Talkaround when selected. Watch for the Talkaround indicator on the display.

Site Switch

NOTE: Your radio is programmed to automatically allow you to roam throughout the RCS System, much like a cell phone system, without any action on your part. There may be times, such as when the system goes into SITE TRUNKING, when you may wish to have your radio affiliate with a different mountaintop repeater site.

Press the Side Button 1 briefly to display the current site with which your radio is affiliated. The radio will display the repeater site you are affiliated with for approximately 2 seconds, The radio will then display the Received Signal Strength Indicator, or RSSI, and a number between 0 and 120. (Any number above 50 is considered good.)  After approximately 2 seconds, the radio will return to normal operation.’

To force the radio to affiliate with a different repeater site, press and hold the SITE button until SCANNING appears in the display. The radio will attempt to affiliate with a different repeater site. The radio may affiliate with a different site, or it may re-affiliate with the same site. Repeat Step 1 to confirm which site you are now affiliated with. If you need to affiliate with a different site, repeat Steps 1 and 2 until you affiliate with an adequate site.

APPENDEX

| Removing the Mike connector plate to attach the external Speaker / Mike -------------------( Insert a flat blade screwdriver into the area between the bottom of the cover and the slot below the connector. Hold the top of the cover with your thumb while you pry the bottom of the cover away from the radio with the screwdriver. Then, put the cover somewhere where you can find it! |  |
| --- | --- |

Remember, your radio is your lifeline, learn it well.