Mountain Empire Emergency Communications Plan

We learned during the massive wildfires of 2003 that normal communications systems are prone to failure. Here in Campo valley we lost our power for 6 days as the main transmission lines were lost. Telephone and cellular communications were on and off during the same period.

Telephones. The AT&T land line phone system is battery powered and usually works quite well during a power failure if you have an old style, hard line telephone. The new wireless handset phones plug into a wall outlet and are worthless in a blackout. Find a hard wire phone for your disaster kit, one that plugs into your wall jack and is wired directly to a handset with a dial pad.

FRS 2-way Radio. Advertised with a 2 to 30 mile range these "walkie talkies" will usually travel 2 miles if you are out in the open. Here in the Mountain Empire (Far East San Diego County) the Campo Fire Department and the Mountain Empire CERT has designated FRS Channel 1 as our monitored FRS frequency in an emergency. Use this channel to contact your local community volunteers for information and assistance during disasters. Remember, if your phone is working and you have an immediate emergency Call 9-1-1. Our FRS network is not an official communications system but a way for community members and volunteers to communicate in a emergency with equipment we have on hand.

Scanners. In the Mountain Empire Area fire and law enforcement agencies are dispatched on multiple frequencies and bands. For a list of these frequencies and information on equipment required to monitor these agencies in an emergency go to http://www.craigwilliams.com/radio/scanner/heartland.htm

Amateur ( HAM ) Radio. San Diego County and the Mountain Empire Area are well covered by Amateur Radio Systems and operators. The San Diego County Mountain Empire Disaster Preparedness Council and local area CERT Teams have representatives from the San Diego County Radio Amateur Civil Emergency Service (RACES) group. The San Diego County RACES group is based in the County Communications Center / Emergency Command Center in Kearny Mesa. For more information on RACES contact Craig Williams at 619-478-2505

If you are an Amateur Radio Operator you are encouraged to contact us and become a part of our local Disaster Preparedness Plan. If you are interested or wish further information on our local Amateur Radio activities please call Craig Williams, W6CAW, at 619-478-2505, . Also, you can usually find us at 7 and 9 AM, on the local SANDRA VHF Repeater. ( 146.640, minus offset, 107.2 PL )

Frequency Plan

During a local or area-wide emergency the Campo / Lake Morena Disaster Committee and our local CERT Teams will use the following radio frequencies for in and out of area communications. Amateur frequencies will be manned by licensed operators.

Communications at Local Sites -- Campo Fire Station EOC - Community Center - Flying A Ranch - Others as Required.
FRS Channel #1. Family Service portable radios (W/T)
Red Dot "Jobcom" low power W/T, 151.625 MHz
Amateur Radio National Simplex, 146.520 MHz

Between Sites -- Between any staging location or shelter as in above.
FRS Channel #1. Family Service portable radios (W/T)
Amateur Radio, National Simplex, 146.520 MHz, 160 Meters 1.945 Mhz
"Red Dot" low power VHF, 151.625 MHz.

Between Sites and Communities in San Diego County -- Primary Amateur Radio Frequencies
Lyons Peak, SANDRA, TX-146.865 /RX-146.265, PL 107.2 
White Star (Boulevard), SANDRA, TX-144.68 /RX-145.28, PL 107.2
Otay Mountain, SANDRA, TX-146.04 /RX-146.64, PL 107.2
RACES/County EOC, Primary VHF - RACES, Red 1, RX-147.195. A voted system. Contact RACES for further repeater details.
160 Meters 1.945 Mhz.
80 Meters 3.960 MHz. 40 Meters 7.233 Mhz, 
20 Meters 14.300 MHz international center if interest frequency.

Other
Animal Rescue Reserve and Humane Society, http://www.sdhumane.org .
Animal Rescue Reserve (ARR)  RX-155.715
ARR – Simplex RX 154.54

Radio Frequencies, Details.

| Repeater Location, Owner | Receive | Transmit | Offset | Direction | PL Tone | Assignment |
| --- | --- | --- | --- | --- | --- | --- |
| 2 Meter Simplex | 146.520 | 146.520 |  | Simplex | ------- | Local short range |
| Otay Mt. SANDRA | 146.640 | 146.040 | 600 kHz | Minus | 107.2 | Primary HAM Net Control |
| Lyons Peak SANDRA | 146.265 | 146.865 | 600 kHz | Plus | 107.2 | Secondary HAM Net Control |
| Hi Pass (Boulevard) SANDRA | 145.280 | 144.680 | 600 kHz | Minus | 107.2 | Secondary Campo Area |
| White Star (Boulevard) RACES GOLD 7 | 448.780 | 443.780 | 5.00 MHz | Minus | Controlled | RACES Mt. Empire Area |
| RACES RED 1 Voted System | 147.195 | 147.795 | 600 kHz | Plus | 114.8 | RACES 1 Primary Voted |
| ARR G-7 Repeater, Los Pinos | 155.715 |  |  |  |  | ARR Primary |
| ARR G-1 Simplex | 154.540 |  |  |  |  | ARR Simplex |
| Community Radio Frequencies | Receive | Transmit | AKA |  | PL Tone |  |
| Red Dot "Jobcom" low power W/T | 151.625 | 151.625 | Red Dot |  | None | Local Site and Site to Site |
| Family Service Radio (FRS) W/T Channel 1 | 462.5625 | 462.5625 | Channel 1 |  | None | Local Site and Site to Site |

HF Amateur Radio

160 Meters. 1.945 Mhz. San Diego County Net. Daily 19:30 Hours.

Emergency Nets

3.905 Mhz 09:00 Hrs SD ARES Sunday RACES ARES

3.933 Imperial RACES Sunday  08:30 RACES ARES

3.945 Mhz 08:30 Hrs Riverside RACES Sunday RACES ARES

3.960 SD RACES EOC STATE OES Monday 20:00 Net Primary SD HF Emergency Frequency

3.965 09:00 Hrs Orange Co. ARES Sunday RACES ARES

3.990 AZ RACES NET Sun. 07:30 MT RACES ARES

7.233 Mhz 09:00 Hrs SD ARES Sunday RACES ARES

7.2500  Cal. EMCOMM Net 8:30 AM RACES ARES

3.9100 Skywarn Primary Night Skywarn

3.9500 Skywarn Tertiary Night Skywarn

3.9650 Skywarn Secondary Night Skywarn

7.2400 Skywarn Primary Day Skywarn

7.2650 Skywarn Secondary Day Skywarn

7.2850 Skywarn Tertiary Day Skywarn

Emergency Center of Activity Frequencies
International frequencies to listen for emergency communications.
Move off frequency after initial contact.
15m - 21,360 kHz
17m - 18,160 kHz
20m - 14,300 kHz
40m - 7,060 kHz
80m - 3,760 kHz